## Slide 1: Model based conformance testing of communication protocols in common programming language
Nikolay Pakulin
Senior Researcher, ISP RAS, Moscow
npak@ispras.ru

## Slide 2: Conformance testing of Telecom Protocols
Protocol: a set of data representations, message formats, message exchange and processing rules ensuring information exchange between computing systems
  Internet (Ethernet, IP, TCP, UDP, HTTP, …)
  Telephony (GSM, UMTC, WiMAX, …)
  Control (Modbus, Profibus, …), Avionics (AFDX, …), Automotive (CAN, IAS, …)
  …

## Slide 3: Conformance testing of Telecom Protocols
Conformance testing: complex of active studies of protocol implementations to evaluate the degree of compliance with protocol specifications
  Hypothesis of well-designed protocols: any conformant implementations under normal conditions always communicate. No deadlocks, livelocks, format ambiguities, etc.

## Slide 4: Industrial Methodology
Test Suite is comprised of separate test cases
Test purposes informally define situations to be tested. A test purpose corresponds to one or more test cases
Implementation is considered conformant when all tests pass – all test purposes are ‘covered’
Test Suite
Tests
TP
TP
TP

## Slide 5: Industrial Approach to Conformance Testing
Manual test cases
  Little level of code reuse, lots of duplicated code
ISO 9646, TTCN
  Further development: TTCN2, TTCN3, UML Testing Profile
  TAHI (Perl + C++), ETSI (TTCN3 + Java)
Verdicts are not based on a formal protocol specification
Test coverage is informal
Automation is not intended
Thousands of test cases for real-life protocols
Test System
SUT
input
alt
reaction1
pass
reaction2
inconc
fail
Test case
preambule
postambule

## Slide 6: Model-Based Testing
Formal Specification (Model)
Protocol Specification
Test Suite
Requirements modeling
Test Construction

## Slide 7: Model-Based Testing
Tests are constructed from a model of the protocol in automated fashion
Models capture requirements from the protocol specification
  Machine readable, unambiguous
  = Formal Specification
Test construction is
  Nearly exhaustive
  With well-defined coverage
  Trackable to the initial specification through model
  Less amount of manual code compared to manual test case development
Testing effort and quality
  up to 5 times less than manual test case development
  Better test coverage

## Slide 8: Practitioners’ Requirements to MBT
Models
  Comprehensible, easy to read
  Straightforward, easy to write
Test generation
  Modular: produce tests for separate features
  Comprehensive: easy to read
  Reproducible: tests for same SUT should behave in the same way
  Trackable: detailed logs for post-mortem analysis
Ease of use
  Accessible tools
  Reasonable labor cost

## Slide 9: Approaches to MBT
Using special-purpose languages for models (SDL, LOTOS, VDM …)
  Not easy to read, not easy to write, expensive and rare tools
Using graphical notations (UML + constraints)
  Difficult to develop complete models for real-life protocols
  Limited tool support
Using programming languages
  Java Markup Language
  NModel – pure C#
  SpecSharp – extension of C#
    Integrated with MS Visual Studio!

## Slide 10: Approaches to MBT
Fully automated test construction
  Solvers require linear constraints, no maps, sets, lists, etc.
  State explosion problem: small (impractical) protocols only
    Or tricky manual adjustments
Model exploration
  Long test sequences
  Random walk – irreproducible results
On-the-fly test generation
  No need for solvers
  Test sequence implementation dependent

## Slide 11: PyTESK: MBT in Python
PyTESK is a Python library
  Behavior modeling: contracts, EFSM, message sequencing
  Model composition: processes, channels, message exchange
  Test construction: traversal of a state machine on-the-fly
Why Python
  Clean language with simple grammar, well documented
  Powerful extension mechanism, rich library
  Widespread: tools, books, tutorials
Alternatives:
  Perl (write-only language),
  Ruby (poorly documented, less tools)
  Java, C# - complex languages

## Slide 12: PyTESK Models
# State machine model: transition
@Transition
@From('DATA_SENT')
@On(Ack, number = Self.number)
@When(Self.last_block)
def last_block_confirmed(self, msg):
self.timer.reset()
# File transmission finished
# Inform upper layer
self.application_channel.put(ServerFinished())

## Slide 13: PyTESK Models
Contract specification: obligations between caller and callee
@Requires(Arguments.sum > 0)
@Ensures(If(Pre.balance - Args.sum < -Self.limit).Then(Result == 0))
@Ensures(If(Pre.balance - Args.sum >= -Self.limit).Then(Result == Args.sum))
@Ensures(Pre.balance - Result == Self.balance)
@Save(balance = Self.balance)
def withdraw(self, sum):
…

## Slide 14: Test Construction
Test sequence is constructed on the fly
  As traversal of a state machine
Manual definition of test state and test actions
FSM Traversal
Test State Machine
Test State
Test Actions Iterator
Apply Test Action

## Slide 15: Test Specification in Python
@Test
@Param(sum = ( 1, 2, 3,
Self.account.limit,
2*Self.account.limit))
@Guard( Arguments.sum > 0,
Self.account.balance < 3)
@Coverage(Self.cov_deposit)
@DependsOnMethods('withdraw')
def deposit(self, sum):
…

## Slide 16: Discussion
PRO
  Easy to use language for behavior models and test generator
  Compact test definition
  Integrated into Eclipse (editor, debugger)
CONS
  Dynamic language – model checking?
  Dynamic language – offline test generation?
  Extra effort for model and test development
  How to debug models and tests?
PENDING
  Reporting, test results analysis

## Slide 17: Conclusion
Model-based testing for thorough testing
  Conformance testing
  Certification
Reduce costs of such testing
Lightweight formal methods